## Slide 1: LINK - STATE ROUTING PROTOCOL
Presented By:
ASHWATH
SURESH HEGDE

## Slide 2: INTRODUCTION:
  Link – State Routing also known as shortest path first algorithm.
The shortest path to a destination is not necessarily the path with the least number of hops.
In link state routing, each node has a complete map of the topology.
If a node fails, each node can calculate the new route.

## Slide 3: LINK STATE ROUTING PROTOCOL: PROCESS
  The routers learn about the directly connected networks.
  Routers exchange hello packets to neighbors – To discover neighbors that use the same link state routing protocol on its link.
  Routers then build Link State Packets (Link State Packets contains the link id, link state, cost).
  Routers then flood LSPs to all neighbors.
  Routers calculate the best path to each destination with the help of the LSP database to build the network topology.

## Slide 4: LINK STATE ROUTING PROTOCOL: PROCESS
Received LSAs
IP Routing Table
Dijkstra’s
Algorithm
Link State Database
LSAs are flooded to other interfaces

## Slide 5: LINK STATE ROUTING PROTOCOL: ADVANTAGES
Router can independently determine the shortest path to every network.
Smaller routing tables.
A periodic/ event driven routing updates.
Faster convergence.

## Slide 6: LINK STATE ROUTING PROTOCOL: DISADVANTAGES
Link State Routing Protocol require higher processing power when compared Distance Vector Protocols.
Link State Routing Protocol require more memory.
Initial flooding may degrade the performance of the network.

## Slide 7: DIJKSTRA'S ALGORITHM
Single Source Shortest Path.
For a weighted directed/ undirected graph G (V, E) -
V: Set of Vertices, E: Set of Edges
Let s be the source vertex.
The algorithm will return the shortest path from s to all vertices in V

## Slide 8: DIJKSTRA'S ALGORITHM:
dist[s] ←0 for all v ∈ V–{s} do dist[v] ←∞ S←∅ Q←V while Q ≠∅ do u ← mindistance(Q,dist) S←S∪{u} for all v ∈ neighbors[u] do if dist[v] > dist[u] + w(u, v) then d[v] ←d[u] + w(u, v)
return dist

## Slide 9: DIJKSTRA'S ALGORITHM: APPLICATIONS
Mapping (Google Maps)
Traffic Information Systems
Routing Systems

## Slide 10: Thank You!